Performance tools & Sequential Optimization of Jacobi
Shrikant Vinchurkar
Mayank Chaudhary

---
Results from Assignment 1
Calculation of FLOPs Metric
FLOP = #Iterations * 11.0 * grid resolution for that particular iteration
11 operations = 4 operations( 3 add + 1 multiply) in relax_jacobi + 7 operations (4 add 2 mult 1 sub) in residual jacobi
FLOP/s = floating point operations for particular resolution(specific iteration) / running time in sec

---
Compiler Options
- - O[n] specifies compiler optimization
- - fast ( Maximizes speed across the entire program)
- - ipo (Enables interprocedural optimization between files.)
- - fno-alias (turns off aliasing in the program )
- Pragma ivdep ( instructs the compiler to ignore assumed vector dependencies)
- Opt-report (Tells the compiler to generate an optimization report to stderr)

---
Compiler Options
- - O[n] specifies compiler optimization
- - fast ( Maximizes speed across the entire program)
- - ipo (Enables interprocedural optimization between files.)
- - fno-alias (turns off aliasing in the program )
- Pragma ivdep ( instructs the compiler to ignore assumed vector dependencies)
- Opt-report (Tells the compiler to generate an optimization report to stderr)

---
Comparison of results for various options

---
Peak Performance of Supermuc
1. Thereotical peak performance of one core on Supermuc is 21.6 Gflops
2. We got around 3 GFlops

---
Running code as batch job
Peak performance was lower in a batch job(2 GFlops) compared with login node(3 Gflops)

---
Gprof Utility
performance analyzing tool in Unix
Program can be compiled with -p -g to be used with gprof
After Run,gmon.out is generated
Can be viewed using gprof ./heat gmon.out

---
Runtime overhead of gprof
Program runtime as in gmon,out	Total program runtime with Profiling	Profiling overhead (sec)
41.78	43.386	1.606 ( 3.84 %)
41.97	43.564	1.594 ( 3.79 %)
41.83	43.386	1.556 ( 3.71 % )

---
Direct measurement of Performance Events
- Library used to measure hardware performance counters – PAPI (Performance Application Programming Interface)
- We used High level API's to calculate events for average CPI( Clocks per instruction ), flop rate and L3 cache hit rate

---
Average CPI
- High level funtion used – PAPI_ipc( float * rtime, float * ptime, long_long * ins, float * ipc)
- Upon first call of PAPI_ipc(), counters are set for PAPI_TOT_INS and PAPI_TOT_CYC
- Upon second call, the counters are stopped & count for ipc is stored in float * ipc
- CPI is multiplicative inverse of ipc

---
Flop rate
- High level function – PAPI_flops() fails
- We used counters with event PAPI_FP_OPS
- Calculated Flop rate as #flops / program run time

---
L3 cache hit rate
- Event PAPI_L3_TCH not supported with given hardware
- Verified using the function PAPI_query_event()
- Cache hits calculated as total cache accesses – total cache misses
- Events used PAPI_L3_TCA & PAPI_L3_TCM respectively
- L3 Cache hit rate = total L3 cache hits / program runtime

---
Optimization of Jacobi
- Problem with np = 1022 – code thrashing
- With np = 1022, grid size = 1024 (adding the boundary)
- Issue can be solved with array padding

---
Different approaches for Jacobi Optimization
- Access Pattern into Matrix
- Calculation of residuum
- Avoid Copy Operation
- Cache Optimization by loop blocking
- Cache Optimization by Interleaving of iterations

---
Access pattern into matrix
- Matrix calculation & Copy operation in relax_jacobi() had flaws with memory access
- Memory access not contiguous, stride of sizex
- Problem solved by Loop Interchanging to make memory access contiguous, stride 1 access
- Decreases cache misses

---
Access pattern into matrix (copy loop interchange)

---
Access pattern into matrix (relaxation loop interchange)

---
Calculation of residuum

---
Changes in code

---
Modified residual calculation
Calculation results (in green)

---
Results after change in residual calculation
Although the performance in Mflops/s dropped, the no of floating point operations per loop changed from 11 to 4. Hence the total no of Gflops over an iteration as well as entire program dropped.
Advantage of this approach: the running time of program dropped from 14 sec to 11 sec (verified by repeating readings)

---
Initial loop blocking
Approach: horizontal splitting into 2 blocks & do 2 iterations in a single call of relax_jacobi

---
Horizontal Loop Blocking
Dividing the array into 4 horizontal blocks

---
Interleaving approach
1--> 3
0->2->4
0->2->4
1--> 3
1--> 3
0->2->4
0->2->4
1--> 3

---
Pattern looking for
- 1_1
- 2_1 1_2
- 3_1	2_2	1_3
- 4_1	3_2	2_3	1_4
- 4_2	3_3	2_4
- 4_3	3_4
- 4_4